# Bitscope Micro tips (DSO)

## Understand Act On Touch Parameter settings
Parameters can be set by
- left clicking in a field and dragging up and down (continuous variation)
- right clicking and selecting from a menu
The trigger level and the cursors can be set by dragging

See more of your curves by widening the display window:

Use zoom for the same purpose.

## The scope window

Time base
= time / div
200us / div

Measured DC or bias
voltage
This is weird!

Focus time
= time at the display center relative to trigger point

Sampling frequency
(Sample Rate)

What does VA, VB exactly mean? As described in the manual, it is not clear! (See channel settings and appendix)
## Virtual instruments and Display Format Menu
Virtual instruments / The dual scope window is selected with the SCOPE button on the right, or the DUAL button. SCOPE: multiple channel oscilloscope / DUAL: 2 channel sample linked oscilloscope / Does this make any difference for the Bitscope micro? / SCOPE: 1 channel activated by default, you have to activate the other one manually. / DUAL: 2 channels activated by default. / The VECTORSCOPE function is only availabel for DUAL. / Other possibilities: / MIXED: 2 analog channels, 6 digital channels displayed simultanuously / LOGIC: 8 channel logic analyser / The spectrum analyzer would be expected here, but it is found in the Capture control window.
Display format menu / Right klicking on the FORMAT field (default = OSCILLOSCOPE) gives the other possibilities: / MIXED DOMAIN SCOPE = oscilloscope with 2 channel spectrum analyzer / SPECTRUM ANYLYZER / VECTORSCOPE PHASE ANALYZER

For most time domain measurements, DUAL or SCOPE are the right choices.
For logic analysis, choose MIXED or LOGIC
For frequency analysis, choose SPECTRUM ANALYZER or MIXED DOMAIN SCOPE

## The channel settings

Activity
RED = Overdriven

Analog range
(voltages above this clip!)

Probe attenuation

Offset
Adjust or track input offset
REF / MEAN / MIN / MAX / MEDIAN
Set to REF for DC measurements

Channel ID and focus selector
(for cursor measurement)
Channel that has the focus is underlined

Switch channel ON / OFF

- Switch channel ON
- Select voltage / DIV (continuously by dragging in the V/DIV field or from list by right click in the field). The analog range is normally set automatically
  When the activity LED turns red, the channel is overdriven. In this case, set V/DIV and / or offset to other values, or use a 10:1 probe.
- Eventually set probe attenuation (right click)
- Adjust offset to have a nice curve
  The display can track mean / median /min / max for offset
  or use no offset (REF)

  Use REF for ground referenced measurements (this corresponds to DC input setting on a classical oscilloscope)
  The curve can be moved up and down by changing the offset value (drag with the mouse in the offset field).

  Use MEAN offset to eliminate DC bias from the waveform. This is similar to AC coupling on a classical oscilloscope.

  Use MEDIAN if the signal has a variable mean value, e.g. modulated PWM
  MEDIAN is in the middle between MIN and MAX
The combination of Offset value and ZERO button can be very confusing, especially when the question arises: where is my ground level?
As I think I found out after much experimenting and reading, it works as follows:
For DC measurements:
- use REF as offset tracking mode (right click, select REF)
- Do not push the ZERO button! Instead, right klick on it and do „Reset zero“.
  This moves the zero line always to the middle of the display.
  Now the offset should read „0V“

If this procedure is not followed, the cursors read false voltage values!

http://www.bitscope.com/software/blog/DJ/?p=DJ19A
Zero Set Function
https://trello.com/c/7Q6Wz4OY/17-input-offsets-coupling

It is not clear to me if this strange behavior is a software bug or a misunderstood special feature.

## Timebase settings

Activity

Default:
Continuous capture

Start (or stop) single
Capture
Activated automatically by the REPEAT button

To Wait for trigger, turn off AUTO trigger!

Display frame rate

Pre-Trigger
Buffer size before trigger event
POST = none
Actual amount may differ

ZOOM in and OUT
for capured curve

FOCUS TIME
Time relative to the trigger
(zero is in the middle of the display)

- Timebase in s/DIV implicitly sets the frame rate.
- The display normally only shows a part of the captured waveform!
  Use ZOOM and FOCUS TIME settings to see more of it!
  Don't forget the Act on Touch philosophy. By klicking and dragging these settings can be adjusted continuously

## Repeat and single shot mode
- For periodic signals use REPEAT (this automatically activates TRACE), and AUTO trigger.
  This gives an automatic update on the screen.
  It is the default at startup
- For single events, switch off AUTO trigger and REPEAT.
  Now the oscilloscope waits for a trigger event.
## Trigger control

LED is on while waiting

Trigger type:
COMP / SALT

Automatic triggering
Switch off to wait for a trigger event!

Trigger level
Drag to change

Filter:
NORMAL / FILTERED / HIGH SPEED

Trigger source

Edge

Trigger level may also be set to:
REF / MEAN / MEDIAN
(Right klick)

## Trigger type:
## COMP = Analog Comparator (this is the normal choice)
## SALT = Sample Analog Level Trigger A digital comparator uses the sampled signal, useful for AM, FM and other modulated complex signals
## The trigger level may be set to a fixed value, or it can be tracked using MEDIAN or MEAN:
## MEAN = similar to AC triggering, regardless of DC bias
## MEDIAN = tracks the signal at mid-point Useful for PWM or other highly asymmetric signals, where the mean value changes all the time.
## If CURSOR is active, the trigger level may also be set by moving one of the cursors (MARK or POINT). To do this, right klick on Cursor level field and select MARK or POINT.
## If the signal has glitches the trigger may be too fast. In this case select FILTERED. The hold-off time is indicated in the FILTER field, and it may be adjusted by klicking and dragging.
## In mixed mode (display analog and logic signals) you can trigger on analog or logic signals.
## Cursor measurements
Tip: it may be a good idea to turn off GRID when using the cursors.
The cursors are named
MARK (1st cursor), green
POINT (2nd cursor), orange

POINT (orange)
voltage cursor 2
MARK (green)
voltage cursor 1

POINT (orange)
time cursor 2
MARK (green)
time cursor 2

Voltage at orange cursor (POINT)
Voltage at green cursor (MARK)
Difference voltage
between cursors
dV/dt between cursors
can be used to measure slew rate (not in this example)

Time at orange cursor
Time at green cursor
Time between cursors
Frequency given by time difference

The time origin is in the middle of the display.

## Tracking cursors
Cursors can not only be moved manually, but also automatically by using the tracking mode.
This changes the cursor value automatically as the signal changes.
Voltage cursors:
Right click into the voltage MARK or POINT field and select from menu:
REF = signal ground (no tracking)
MIN, MAX, MEAN, RMS
MEDIAN = midpoint between MAX and MIN
MARK, POINT = non tracking, interactively moved in the window
CENTRE = set to mid-point between current MARK and POINT values
TRIGGER = current trigger level

Time cursors
Right click into the time MARK or POINT field and select from menu:
FOCUS = in the middle of the display
TRIGGER = at the trigger point
MARK, POINT = non tracking, interactively moved in the window
CENTRE = set to mid-point between current MARK and POINT values
FIRST, LAST = set to first or last sample in the capture buffer

In the display, cursors are always visible so they can be dragged, even if the corresponding value is beyond the diagram limits.

## Capture control
(Bottom right)

Activity

Format:
OSCILLOSCOPE
MIXED DOMAIN SCOPE
SPECTRUM ANYLYZER
VECTORSCOPE
PHASE ANALYZER

Sample rate

Rendering mode:
SMOOTH / SHARP / POINTS
Use POINTS to see the sampled data,
SMOOTH to have a nice display

Buffer size

DISPLAY PHOSPHOR MODE:
NORMAL / OVERLAY / DECAY

DATA MODE
RAW DATA: no signal processing
DECIMATED: decimate data before sending them to display
ENHANCED: improve resolution, but fast
WIDE BAND: high resolution and show high frequencies

Control DATA RECORDER

## DSO Data recorder

Control DATA RECORDER

To temporarily record and replay:
Listen – Pause – Review

Review does not automatically show the recorded data!
You have to use TRACE or REPEAT to see them.

To record data to a file:
<Rklick> New - <file name> → the indicator shows Ready
Use REPEAT or TRACE (with or without AUTO) to start displaying and recording the data.
<Rklick> Close

To replay recorded data:
<Rklick> Open <filename> → the indicator shows Play
<Rklick> - Play → the indicator shows PLAYING
TRACE shows the replayed waveform.
Recorded waveforms may be displayed with other time base settings than the ones they were recorded with.

Data format:
Each data frame is listed in CSV format, together with metadata.

Example:

trigger,stamp,channel,index,type,delay,factor,rate,count,data
5017,09:55:33,0,5611,0,0.000021,12,44000,439,2.5797,2.5797,2.5797,2.0943,0.39724,-0.04371,-0.045703,-0.042779,…..

5017	trigger event number
09:55:33	time stamp
0	channel CHA
5611	index identifying all data belonging to the same frame
0	data type (analog / logic /decimated / filtered ...)
0.000021	delay = post trigger delay
12	factor (decimation / oversample factor if any)
44000	rate = sample rate
439	count = number of samples in this record

data:
2.5797,2.5797,2.5797,2.0943,0.39724,-0.04371,-0.045703,-0.042779,…..

# Appendix

## The ZERO volt riddle

Example of a 3.3V digital signal.
The first question arising is: where is the 0V line?
I tried to use the cursors to solve this.
Under certain circumstances I have the right result , but under other circonstances I have a wrong iondication from the cursors:

You see that the green cursor indicates 0V.
This would mean that my signal would have a negative offset (see curve and: VA = -2.11V), which obviously is wrong!
 I found out that Right klick on ZERO button, Reset ZERO brought the zero line to the middle of the display and everything was correct again.
According to Martin from bitscope.com/support the right procedure is the following:

To get an accurate reading you need to Zero the curve.

Assuming you have a 1:1 probe connected, set the scale to 2V/Div.
Short the probe (at the tip or use Ref on the Probe).
Set the Channel Offset to REF (Right Click the Offset Panel).
Make sure the trace is on the zero line and click ZERO.
Turn cursors on and R-click the brown Cursor Panel to MAX - so it tracks the DC voltage

The Next step is important!

Left-Click the Offset panel and drag it down 2V. The trace and cursors should all move down 1 Div. Now apply the voltage to CHA and the cursor will record the voltage.  What you have done is bias the BitScope range UP to favour positive voltages.

The key point here is that for DC measurements, you shift the offset of the channel to be unipolar to extend the range.

The other way to measure DC voltages is to use the 10:1 Scope Probe which effectively extends the range of BitScope.

Set the scaling to 10:1, 2V/Div. Do this before you adjust offset and ZERO.

To set the offset you must short the probe tip to GND (don't use the Ref setting), adjust the trace to the center, and then click ZERO.
No need to adjust the offset  in this case (unless you are measuring 50V or similar - in which case do as above).

Now apply the voltage and read from the cursor.

​__________________________________________________________________________________

Please report any errors or suggestions to

jean-claude.feltes@education