# CAD / CAM with HeeksCAD / HeeksCNC
HeeksCAD is a CAD and CAM program that is free for Linux users
## Define tool(s)
Menu Machining – Add new tool – Drill
define name, diameter and offset to workpiece (normally 0)

Note: to mill acrylic glass, polyvinil chloride and the like, one flute mills (Einzahnfräser) must be used! Otherwise the material melts.
## Drilling
Example: / Three holes of 4mm diameter should be drilled in a plexiglass sheet of 3mm thickness at the xy coordinates (10, 10); (20, 10) and (30, 10). / The upper face of the sheet will later be be set to Z=0 in LinuxCNC

Workflow in HeeksCAD

If not already done, define tool: 4mm drill
- Menu Geometry – Draw points at the xy coordinates
  This generally means some fumbling with the mouse to get the right coordinates.
  Coordinates can be edited in the properties window after drawing them, but this is not really easy in the current version 1.1.0.
- In the object browser select points to drill (Shift - LKlick):

RKlick – New Drilling Operation

The most important options to set are:
  - Tool	(4mm drill)
  - Clearance Height	(20mm above the upper face of the material where Z=0)
  - Start Depth	(2mm above the upper face we begin with drilling)
  - Final Depth	(-5mm)
    The thickness of the sheet is only 3mm, but we have to go a little bit further as the drill tip is conical
  - Vertical Feedrate

- Produce G code
  Menu Machine – Postprocess
  Now a G code entry should be visible in the object browser.
- Save Gcode
  Menu Machine – Save G code

Now start LinuxCNC

- Home all axes
- Set workpiece zero for X, Y, Z	(touch off button)
- Open G code file
  Control visually if everything is OK
- Start program and be prepared to push emergency stop if anything goes wrong.
## Drilling bigger holes of different sizes and forms
This can be done by milling through the material with a smaller milling tool.
Procede as discribed in “Milling pockets”, but set final depth as to transperce the material.

### Milling pockets

Example: / Rectangular pocket 10x10, / circular pocket with diameter 10 / and freeform pocket defined by sketch, / all pockets 2mm deep, in a material that is 3mm thick

Workflow in HeeksCAD

Draw outlines in HeeksCAD

Menu Geometry – Draw Rectangle
Toolbar – Draw circle (see picture on the right)
Menu – Draw a sketch
Notes:
- Don't use Geometry – Ellipses, those cannot be used for a pocket operation (at least not in version 1.1.0)
- Circles do not appear in the menu, only in the toolbar.
- There are 3 ways to draw a circle:
  - through 3 points
  - defining a center point and another point to define the radius
  - defining a center point and entering the radius in the properties box

- Select objects in object browser or by selecting them with the mouse
- Right klick on the selected objects in the object browser – New Pocket Operation

The most important options are:
  - Clearance Height	(20mm above the surface)
  - Tool	(2mm end mill)
  - Start depth	(0mm, Z=0 is the upper side of workpiece)
  - Step down	(1mm: each pass of the mill takes 1mm)
  - Finishing depth	(0.1mm: the last pass takes only 0.1mm for better surface quality)
  - Horizontal Feedrate	(100mm/min)
  - Vertical Feedrate	(100mm/min)

    The feedrates must be set according to the material.
- After this, 3 new “Pocket” objects are visible under Operations in the Object browser
- Make G code
  Menu Machinig – Postprocess
- Save G code
  Menu Machining – Save G code

  Now the toolpath is visible in the drawing and there is an object “NC Code” in the object browser

Now start LinuxCNC

- Home all axes
- Set workpiece zero for X, Y, Z	(touch off button)
- Open G code file
  Control visually if everything is OK
- Start program and be prepared to push emergency stop if anything goes wrong.

## Milling a profile
## Workflow in HeeksCAD
Example: / Hexagonal piece, 3mm thick, inscribed into a circle of 20mm radius

## Draw the sketch: Menu Geometry – Draw Polygon Before drawing, adjust number of sides (to 6) in the property box, select center with the mouse and point to one point of the polygon. Now we have a hexagon in the drawing area. In the object browser there is a new sketch consisting of 6 lines.
## Select the sketch in the object browser with the right mouse – New profile operation:
## The most important options are:
  - Tool on Side:	Outside
  - Tool:	(2mm end mill)
  - Clearance Height	(20mm above the surface), for fast moves
  - Rapid safety space	(2mm above the surface)
  - Start depth	(0mm, Z=0 is the upper side of workpiece)
  - Final depth	(3mm, according to material thickness)
  - Step down	(1mm, every pass of the mill takes 1mm, so we have 3 passes)
  - Horizontal Feedrate	(100mm/min)
  - Vertical Feedrate	(100mm/min)
    The feedrates must be set according to the material.
## After this, a new “Profile” object is visible under Operations in the Object browser
- Make G code
  Menu Machinig – Postprocess
## Save G code Menu Machining – Save G code Now the toolpath is visible in the drawing and there is an object “NC Code” in the object browser:

Now start LinuxCNC

- Home all axes
- Set workpiece zero for X, Y, Z	(touch off button)
- Open G code file
  Control visually if everything is OK
- Start program and be prepared to push emergency stop if anything goes wrong.
## Take care:
## The piece of material that is the fruit of our work must be fixed somehow, otherwise it will get loose on the last pass of the mill and be damaged. This can be done in many cases with double sided glueing tape.
## FreeCAD and HeeksCAD
Though fairly easy to use, HeeksCAD does not allow to enter coordinates, lengths and diameters directly with the keyboard. For bigger projects it is better to do the design in FreeCAD and import the result e.g. as STEP file into Heeks, and let Heeks do only the CAM part.

The developers of FreeCAD are developing a very fine integrated CAM module (that can be tested in the freecad-daily version), but there are so many changes at the moment (5.2017) that I would give the advice to wait until there is a stable version.